## Slide 1: Distributed Interactive Simulation (DIS) 201
Bob Murray
DIS PDG Vice Chair
bob.murray@boeing.com
Extensibility & Dead Reckoning
30 March 2013

## Slide 2: Overview
DIS Extensibility
  Why we need PDU customization
  Compatibility with previous DIS standards
  Variable Parameter and Standard Variable records
  Attribute PDU
Dead Reckoning
  General concept
  Rotational dead reckoning details
  New rotational threshold calculations methods
  New computational savings methods

## Slide 3: DIS V7
IEEE 1278.1-2012 Distributed Interactive Simulation – Application Protocols
Real-time, geographically distributed interoperability for entity-level sims
Commonly called DIS Version 7 (V7)
Published by IEEE in December 2012
Combines DIS 1995 (V5) and 1998 (V6)
DIS PDG is also updating 1278.2
  Communication Services and Profiles

## Slide 4: Improvements in DIS V7
Clarified rules for almost all PDUs
Backward and forward compatibility
Five new PDUs (Directed Energy, IO) and new Mode 5/S layers for IFF
Variable heartbeats
Transfer ownership
Time
PDU Extensibility
Dead Reckoning

## Slide 5: Protocol Extensibility
DIS now more easily customized
Corrects a weakness in the original standard
Backward compatibility maintained mostly
Variable Parameter Records
  Entity State, Detonation
Standard Variable Records
  Transmitter, IFF, DE Fire, Entity Damage, IO
Attribute PDU
  Can extend all other PDUs
  Or, info that doesn’t have a PDU

## Slide 6: Problem with fixed PDU structure
Many PDUs are simple fixed format
  Easier to process
  One “C” structure for entire PDU
Some PDUs have variable content
  Data, EE, Transmitter, Articulated Parts in Entity State
Experience has shown that almost all PDUs need to be extendable

## Slide 7: Customization
Needed for analysis, after action review, high fidelity modeling
Much customization was done with Data PDUs
  OK is some instances but it is a Simulation Management PDU
Technically inappropriate for use with non-SIMAN functions
  But, that’s all there was

## Slide 8: Variable Records
Extensibility was recognized as a needed improvement in DIS
The idea of a “variable datum” is good
The trick is how to apply it to all PDUs without breaking compatibility
Variable Record Tiger Team was formed to solve the problem

## Slide 9: Compatibility
All decisions to alter DIS PDUs had the issue of compatibility to older versions
  New standards are slow to be accepted if not compatible with legacy
  Compatibility won in almost all cases
Backward compatibility is easier
  New sims can process old PDUs
Forward compatibility is tricky
  How can old sims process new PDUs?

## Slide 10: Forward Compatibility
Surprisingly, almost all modifications to PDUs are forward compatible
  Assume old sims will simply discard the five brand new PDUs
Functionality added in padding
  Old sims should ignore padding
  DIS always had a rule to set pads to zero
  Zero value defined as old function so new sims interpret old PDUs properly

## Slide 11: Variable Parameter records
Made use of existing Articulated / Attached parts in Entity State and Detonate PDUs
Renamed Variable Parameter records
  Maintains forward/backward compatibility
  Name is misleading: format is variable but length must remain fixed at 16 bytes
First 8 bits denotes record
  Other 120 bits open for definition

## Slide 12: Example VP record
3 new records defined in 1278.1
Separation VP record | 
Parameter Type Designator = 2 | 8-bit enumeration
Reason for Separation | 8-bit enumeration
Pre-Entity Indicator | 8-bit enum
Padding | 8-bits unused
Parent Entity ID | 48-bit enum
Padding | 16 bits unused
Station Name | 16-bit enum
Station Number | 16-bit enum
Separation VP (shown)
Entity Type
Entity Association
No change to Articulated and Attached Parts VP records
Several ideas for future extended appearance VP records

## Slide 13: Standard Variable Specification Record
Number of Standard Variable Records (N) | 16-bit unsigned integer
Standard Variable record #1 | Record Type – 32-bit enumeration
 | Record Length – 16-bit unsigned integer (6+K1+P1)
 | Record-Specific Fields – K1 octets
 | Padding to 64 bits – P1 octets
o o o | 
Standard Variable record #N | Record Type – 32-bit enumeration
 | Record Length – 16-bit unsigned integer (6+KN+PN)
 | Record-Specific Fields – KN octets
 | Padding to 64 bits – PN octets

## Slide 14: Standard Variable Spec Record (cont)
Format used for all new variable records
32-bit Record Type
  Enum values assigned to not conflict with Datum IDs
Length field based on IP rules
  Number of bytes, not bits
  Includes record header, payload, padding
  Always multiple of 8 for 64-bit alignment

## Slide 15: Uses of Standard Variable Spec Record
Transmitter PDU – Variable Transmitter Parameters records
IFF PDU Layers 3, 4, 5 – IFF Data records
Directed Energy Fire PDU – DE records
Entity Damage Status PDU – Damage Description records
IO PDUs – IO records
Attribute PDU – Attribute records
All future PDUs to contain Std Var records

## Slide 16: The Attribute PDU
Allows existing PDUs to be extended without breaking forward or backward compatibility
Not allowed to contain information that already exists in other PDUs
  Otherwise, there would be confusion about which PDU to use
Attribute records conform to Standard Variable Spec record format

## Slide 17: Attribute Record Sets
The PDU contains sets of Attribute records
  Effectively a two-dimensional array of Attribute records
Each set is tied to an entity or object
Envisioned for constructive sims to update attributes of many entities in one PDU
Can still filter whole sets by Entity ID

## Slide 18: Coupled Extension
A transient PDU can be extended by attaching an Attribute PDU to it
  This is called Coupled Extension
  PDU Status bit indicates PDU is followed by an Attribute PDU in a PDU bundle
  The two PDUs shall not be separated
Stateful PDUs can be extended by sending Attribute PDUs at any time
  Or, the Attribute PDU can be coupled if desired

## Slide 19: Attribute Heartbeats
Attributes for stateful PDUs have same heartbeat rules as PDUs they extend
If not coupled, a separate timer could be kept for main PDU and attributes
Or, simpler implementation would be to update main PDU and attributes together
  Uses same heartbeat timer
  But risks excessive updates

## Slide 20: Defined Attribute Records
Three Attribute records have been defined in 1278.1
All extend the Electromagnetic Emission PDU
  Blanking Sector
  Angle Deception
  False Target
As with all customization, more Attribute records are proposed

## Slide 21: Managing Extensions to DIS
SISO-REF-030 has been assigned as a document to catalog DIS extensions
  Produced by DIS Product Support Group
Will manage all changes proposed in Problem/Change Requests (PCRs), not just customization
DIS PSG has started regular telecons
Always looking for volunteers to get it moving faster

## Slide 22: Ideas for DIS V8
Formal language to describe records
  Probably XML-based
Cleaner PDU structure that can be more easily described formally
  Single “discriminator” format for variable content
  Suitable for auto code generators
But would break PDU compatibility
  So need easy gateway translation

## Slide 23: Overview
DIS Extensibility
  Why we need PDU customization
  Compatibility with previous DIS standards
  Variable Parameter and Standard Variable records
  Attribute PDU
Dead Reckoning
  General concept
  Rotational dead reckoning details
  New rotational threshold calculations methods
  New computational savings methods

## Slide 24: Dead Reckoning Basics
Entity sender publishes state and extra information to predict state over time
  Velocity (rate of change), acceleration
Receivers dead reckon (extrapolate) between updates
Entity also keeps a local extrapolation model to know what receivers see
  Updates PDU when error between that model and truth exceeds a set threshold

## Slide 25: Dead Reckoning Example
Green Line: “Truth” Model (Sender)
Red Line: Dead Reckoned (extrapolated) Model (Sender and Receiver)
White Line: Smoothing Model (Receiver)

## Slide 26: Positional Dead Reckoning, DRA 2-5
Dead Reckoning Algorithm 2 and 3
  P = Pupdate + VΔt
  where Δt is time since last update
Dead Reckoning Algorithm 4 and 5
  P = Pupdate + VΔt + ½AΔt2
Error checked in each of 3 axes
  If any exceeds threshold, send update
No change in DIS V7

## Slide 27: Positional Dead Reckoning, DRA 6-9
DRA 6-9 use rotation rate and body coordinate velocity and acceleration to achieve better prediction
  Math is more complicated and not used as much as DRA 2-5
  But it is effective, should be used more
No change in DIS V7 but errors in the math formulas were fixed
See E.7.3 in the DIS V7 standard

## Slide 28: Rotational Dead Reckoning
DRA 2, 5, 6, and 9 have no rotational dead reckoning
  Rotation rates not required for 2, 5
  Rotation rates are required for 6 and 9 but only for positional dead reckoning
DRA 3, 4, 7, 8 all have the same rotational DR formula
  [R]w->b = [DR][R0]w->b

## Slide 29: How Rotational Dead Reckoning Works
Rotation rates are given as a vector ω in body coordinates
  Direction of vector is axis of rotation
  Magnitude |ω| is rate of rotation about axis
Receivers extrapolate orientation by rotating an entity about the axis by angle |ω|Δt, used to form [DR]
There is no acceleration in this math

## Slide 30: Rotation Error Threshold
Just as in positional, the extrapolated orientation will deviate from actual
But calculating the error is not easy
  This is the sender’s problem
Differences in Euler angles is one way
  But singularity point at 90 degree theta
Actual error can be much less than Euler error near the singularity
  Causes excessive updates

## Slide 31: Rotational Error Solutions
Unfortunately, in World coordinates, entities can operate near singularity
  e.g. a ship at the equator heading North
For ground and surface entities, can solve problem by using local Eulers
  These entities are rarely at 90 pitch
Or, DIS V7 has the math for determining exact error at any angle

## Slide 32: Better Rotational Error Calculation
Given two orientations, actual and extrapolated, the error is angle of rotation that takes one to the other
Orientations can be described in either rotation matrices or quaternions
  4 numbers in quaternion has same orientation info as 9 in a rotation matrix
  No singularity in either
Math details described in Annex E.7.5

## Slide 33: Rotational Matrix Solution
Remember [R]w->b = [DR][R0]w->b
  [R]w->b is the extrapolated orientation
  Renamed to [R]D for Dead Reckoned
[R]A represents the Actual orientation
The Error rotation matrix is
  [R]E = [R]DT [R]A where T is transposed
If 3-Trace[R]E > 2-2cos(threshold) then threshold has been exceeded
  Trace is just sum of main diagonal

## Slide 34: Quaternion Solution
Similarly, qD = qU qDR
  qU is orientation at Update, same orientation represented by [R0]w->b
qA is the Actual orientation
If 1- qA• qD > 1-cos(threshold/2) then threshold has been exceeded
  qA• qD is the quaternion dot product
Annex E.7.4 explains quaternion math
  Euler angle to/from quaternion, etc.

## Slide 35: DR Other Parameters for Computational Savings
A 120-bit field in Entity State PDU
  Immediately follows DR Algorithm field
Envisioned as extra space for advanced DR algorithms
  But none have been proposed
DIS V7 reuses this space for redundant information that can speed up computation for all receivers
Described in Annex E.8

## Slide 36: Entities With No Rotational DR
For entities not dead reckoning rotation
  DRA 1, 2, 5, 6, 9
Local Euler Angles DR Parameters | 
Dead Reckoning Algorithm | 8-bit enumeration
DR Parameters Type = 1 | 8-bit enumeration
Padding | 16-bit enum
Local Yaw | 32-bit float
Local Pitch | 32-bit float
Local Roll | 32-bit float
Other Parameters used for Local Euler Angles
  Yaw, Pitch, Roll
Avoids conversion from World to Local coordinates in receivers

## Slide 37: Rotating Entities
For entities that dead reckon rotation
  DRA 3, 4, 7, 8
World Orientation Quaternion DR Parameters | 
Dead Reckoning Algorithm | 8-bit enumeration
DR Parameters Type = 2 | 8-bit enumeration
qU0 | 16-bit unsigned integer
qUx | 32-bit float
qUy | 32-bit float
qUz | 32-bit float
Other Parameters used for update quaternion
  World Psi, Theta, Phi converted to quaternion
Avoids 6 trig functions at start of rotational dead reckoning

## Slide 38: Questions?